## Slide 1: Experiences Implementing Tinuso in gem5
Maxwell Walter, Pascal Schleuniger, Andreas Erik Hindborg, Carl Christian Kjærgaard, Nicklas Bo Jensen, Sven Karlsson
Technical University of Denmark
maxw@dtu.dk
Notes: Work in progress at our lab in Copenhagen

## Slide 2: Motivation
We have developed the Tinuso architecture
  For multi-core research
  Targeted for FPGAs
Application dependent accelerators are important for multi-core research
Software/hardware co-design is difficult!

## Slide 3: Motivation
We have developed the Tinuso architecture
  For multi-core research
Application dependent accelerators are important for multi-cores
Software/hardware co-design is difficult!
app

## Slide 4: Motivation
We have developed the Tinuso architecture
  For multi-core research
Application dependent accelerators are important for multi-cores
Software/hardware co-design is difficult!
So we would like to do it automatically
app
parameters
toolchain
evaluate
feedback

## Slide 5: Contributions
Implementation of the Tinuso processor architecture in gem5
Discussion of gem5 and designing application specific accelerators

## Slide 6: Outline:
Motivation
Contributions
Tinuso Architecture
Gem5 Implementation
Design Space Exploration
Conclusions

## Slide 7: Tinuso
Philosophy: move complexity to software
  Predicated execution to lower branch costs
  Very fast 8 stage pipeline
  No pipeline interlocking; Compiler must produce a valid schedule
GCC 4.9 toolchain
Designed for FPGA synthesis
Will be released as open source
Small and fast
Tinuso | MicroBlaze
376 MHz | 194 MHz
1322 LUTs | 2024 LUTs

## Slide 8: Gem5 Implementation
Instruction Predication
  Easily handled in the instruction decoder
Configurable branch delay slots
  New PCState with counter and NNPC
Instruction delay slots for compiler validation
  Tracked by the Decoder
  Validated at instruction decode

## Slide 9: Gem5 Implementation
Instruction Predication
  Easily handled in the instruction decoder
Configurable branch delay slots
  New PCState with counter and NNPC
Instruction delay slots for compiler validation
  Tracked by the ISA/Decoder
  Validated at instruction decode
Gem5 implementation was easy and painless
  A good fit into our workflow

## Slide 10: Gem5 In Our Workflow
RTL simulator validation
  Simulator built directly from VHDL sources
Toolchain validation
Test | RTL Time | Gem5 Time
memcpy-chk.x1 | 6.47s | 3.5s
memmove.x4 | 21.78s | 3.7s

## Slide 11: Design Space Exploration
Tinuso is intended for multi-core accelerator systems
  Easily configured for specific applications
Many configuration parameters
  ISA, cache sizes, pipeline depth, #of cores

## Slide 12: Design Space Exploration
Tinuso is intended for multi-core accelerator systems
  Easily configured for specific applications
Many configuration parameters

## Slide 13: Tinuso multicore systems
PE
NI
R
PE
NI
R
PE
NI
R
PE
NI
R
PE
NI
R
PE
NI
R
PE
NI
R
PE
NI
R
PE
NI
R
PE
NI
R
Barrel shifter
Multiplier
FPU instructions
Profiling infrastructure
Cache sizes
Pipeline depth
Data Link width
Arbitration scheme
PE
NI
R
PE
NI
R
PE
NI
R
PE
NI
R
PE
NI
R
Up to 480 processor cores on Xilinx Virtex-7 device
synthesizable processor cores
packet switched 2D mesh interconnect
Notes: This is one of the templates that we use
This template is scalable

## Slide 14: Design Space Exploration
Tinuso is intended for multi-core accelerator systems
  Easily configured for specific applications
Many configuration parameters
  ISA, cache sizes, pipeline depth, #of cores
Changing parameters manually is tedious and can be error prone
Effective searching requires fast simulation

## Slide 15: Design Space Exploration
Use gem5 for quick performance estimation
  Can help direct the performance optimization
Use more accurate tools, like Vivado, for power estimation and resource usage
app
parameters
toolchain
evaluate
feedback

## Slide 16: Conclusions
We have implemented the Tinuso architecture in gem5
  It was an easy and painless process
The Tinuso gem5 implementation is useful for a number of workflow considerations
We leverage gem5 for design space exploration of custom multi-core accelerators